## Slide 1: Module 8
Designing a Communication Strategy by Using Queues and Service Bus
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 2: Module Overview
Azure Storage Queues Azure Service Bus Azure Service Bus Queues Azure Service Bus Relay Azure Service Bus Notification Hubs
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 3: Lesson 1: Azure Storage Queues
Storage Queues Overview Viewing Queue Storage Data Storage Queue Messages
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 4: Storage Queues Overview
Storage queues provide a method for storing messages that might be accessed by any number of clients
  Provide reliable messaging between role instances
  Built for massive scale and multiple messages
images
thumbnails
128x128
http://...
256x256
http://...
retrieval
http://...
Storage account
Queues
Messages
Notes: The focus here should be on the simplicity of the queuing mechanism since it is based on the same concepts as other Azure Storage services. Theoretically, the Queue service does not have a limit on the amount of messages but it does require all messages to be less than 8 KB.
Reference Links: http://go.microsoft.com/fwlink/?LinkID=510211
Discussion Question: What type of business applications could benefit by the mechanism of storing requests that are handled asynchronously by workers?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 5: Storage Queues Overview (cont.)
Azure Storage Queues allows you to store large quantities of small messages that can be consumed by a scalable number of consumers
(Retry) Queue messages have flexible leasing and can be processed again by a different consumer/worker if there is a failure with the initial consumer
(Loggin)Queues can take advantage of the built-in Azure Storage logging and metrics
(State-full) Queues can have a concept of “state” across workers/consumers
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 6: Viewing Queue Storage Data
Visual Studio Server Explorer provides a view for Storage queue items in the emulator or in a live Azure storage account.
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 7: Storage Queue Messages
  Storage queues offer the following basic message functionality:
    Peek at next message
    Dequeue next message
    Insert message
    View the last cached message count
  Message content is stored as a string
    Message content can be updated to provide a concept of state
    You can time when a message content update is visible to other consumers
  The result of a message should be idempotent
    By design, there is the possibility of reprocessing a queue message
Notes: Emphasize that the message processing should be idempotent. The repeated processing of a message should not cause any side effects in your system as it is possible for a message to time out due to load or hardware failure and be processed again.
Discussion Question: Is it possible to store a complex type in a queue message?
Serialization is definitely a possibility for queue messages. Special care needs to be taken to not surpass the maximum message size.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 8: Storage Queue Messages (cont.)
Add/Delete Messages
GetMessage(s)
  Retrieves the next message(s) from the queue and it will be invisible to other clients for a specified timeout.
PeekMessage(s)
  Retrieves the next message(s) from the queue while keeping the message visible to other clients.
UpdateMessage
  Updates the content or visibility timeout of a specified message.
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 9: Lesson 2: Azure Service Bus
Service Bus Overview Service Bus Features Namespaces
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 10: Service Bus Overview
Service Bus is a managed messaging infrastructure
  Massive in scale and completely managed
  Allows you to scale out your applications and consumers knowing that the messaging platform will scale out with your application
Allows decoupled components to communicate asynchronously and synchrounously
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 11: Service Bus Features
Relayed Messaging
Publish-Subscribe Topics
Queues
Notification Hubs
Notes: In the later modules the student will learn about Service Bus Relays and Notification Hubs. Service Bus Queues will be discussed in the next lesson. Publish-Subscribe Topics is not used as much anymore since Notification Hubs replaces most of its functionality.
Discussion Question: Which of these Service Bus features can be used for synchronous communication?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 12: Namespaces
A Service Bus namespace is a logical grouping of Service Bus service instances
  It scopes your resources to provide a common and predictable address
  It provides management credentials to use for operations
Notes: Discussion Question: Which queues would you scope together in a massive cloud application and which queues would you scope separately?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 13: Lesson 3: Azure Service Bus Queues
Service Bus Queues Overview Queue Message Delivery Characteristics of Service Bus Queue Messages Service Bus Queues vs. Storage Queues
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 14: Service Bus Queues Overview
Service Bus queues offer a brokered messaging communication model
  Distributed applications can share messages in a First In First Out (FIFO) pattern
  Individual messages are only received by one message consumer
Service Or Application
Queue
Web App
Mobile App
Service
Message Receiver
Service Bus Namespace
Message Sender
Notes: The Service Bus queues are tailored to be general-purpose for different types of distributed applications.
Reference Links: http://go.microsoft.com/fwlink/?LinkID=510212
Discussion Question: What types of application scenarios would require you to send messages from many producers to a single consumer?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 15: Queue Message Delivery
Service Bus queues provide a queuing mechanism with tight control on the order and delivery of messages
  Messages will appear only once
  Messages are processed using the FIFO pattern
  Message locks can be renewed
  Supports transactions
Notes: In order to guarantee the FIFO order, you must have messaging sessions. The idea is that when a consumer recovers from a failed session, the consumer will resume its last message therefore ensuring the order of the queue.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 16: Characteristics of Service Bus Queue Messages
Service Bus queue messages consist of few major parts
  Body
    The body can be any serializable object or a stream
    The DataContractSerializer is used to serialize the complex object
  Label
    Simple text label
  TimeToLive
  Properties
    Dictionary of properties that can be used by your specific consumers.
Notes: Explain how the students can use TimeToLive to expire a message if a certain amount of time passes. The TimeToLive however cannot be larger than the DefaultMessageTimeToLive for the queue. The queue will always use the smaller of the two values.
Discussion Question: Why would you want a queue message that expires early?
You can also pass a string or a Stream to the BrokeredMessage as its body.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 17: Service Bus Queues vs. Storage Queues
Storage Queues
Arbitrary ordering
Delivery at least once, possibly multiple times
30 second default locks can be extended to 7 days
Supports in-place updates of the message content
Can integrate with WF through a custom activity
Service Bus Queues
FIFO guaranteed ordering
Delivery at least once and at most once
60 second default locks can be renewed
Messages are finalized once consumed
Native integration with WCF and WF
Notes: Explain to the students that there is no preferred queue mechanism. When designing a cloud solution, the architect has to look at the advantages and disadvantages for each and then decide on a case to case basis.
Discussion Question: Pick a business scenario that you faced recently that could be solved using queues. Which queuing mechanism would you use for your scenario?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 18: Lesson 4: Azure Service Bus Relay
Service Bus Relay Overview Service Bus Relay Architecture Management Credentials
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 19: Service Bus Relay Overview
Relays provide a mechanism to connect distributed client applications or cloud services to a projected on-premises endpoint
  It allows for unidirectional or bi-directional communication
  It relays messages directly to an endpoint without any brokering of the message
Applications establish an outbound connection to the relay and the relay manages the transport of the messages
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 20: Service Bus Relay Architecture
Service Bus Relay
Service Application
Send/Receive
Client Application
Client Application
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 21: Service Bus Relay Architecture (cont.)
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 22: Management Credentials
Service Bus uses a Shared Access Signature (SAS) to authenticate access to the messaging entities within the namespace
  This replaces the ACS functionality previously available
You can also use a simple web token (SWT) or SAML token from a provider
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 23: Lesson 5: Azure Service Bus Notification Hubs
Service Bus Notification Hubs Overview Benefits of using Notification Hubs Notification Hubs Architecture Registrations Message Templates and Tags
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 24: Service Bus Notification Hubs Overview
Managed infrastructure for sending push notifications to mobile devices
  Multiplatform
  Scalable
  Simple SDK
    Available on many major mobile platforms
Broadcast to many users or target specific users
Notes: You can broadcast a message to a large group of users, send a message to a targeted subset of users or even notify a specific user. The platform handles the batching, transport and management of the messages.
Mention how this service is a SaaS solution.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 25: Target Platforms
You can target notifications to a specific platform:
  Android
    GcmService object
  iOS
    ApnsService object
  Windows Phone
    MpnsService object
  Windows Store
    WnsService object
Android/iOS require a JSON payload
Windows Phone/Store require a XML payload
Notes: Discussion Question: When would you want to send a notification to a specific platform?
A common answer is, for application updates. You may have an issue or update for the iOS app and want to notify iOS app clients.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 26: Benefits of using Notification Hubs
Managed Infrastructure
  You don’t have to worry about scaling your application yourself
  You can focus on messages and templates, not the mechanics of your service.
SDKs available for major platforms
Template support
Support for filtering recipients by tag
Notes: On this slide, you should focus on the fact that the SDKs provide a very simple way to subscribe to a notification hub. The SDK code handles the different toast/notification logic for each platform.
Templates allow you to send the same message to multiple clients and have it display differently for each platform.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 27: Notification Hubs Architecture
Retrieve Handle
Register Client
Register Client
Send Message
Send Message
Send Message
Notes: Client devices register their PNS-handle with the application back-end. The Application back-end registers the client with the Notification Hub.
Whenever a client starts, the client retrieves its handle directly from the Platform Notification Service.
The application back-end then sends a message to the Notification Hub. The Notification Hub handles passing the message to the Platform Notification Service which in turn notifies the appropriate clients using their handles.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 28: Registrations
Each SDK provides a unique mechanism to register for remote notifications
You must register with the Notification Hub using the name of the hub and your unique connection string from the connection information panel
  Two connection strings are available by default:
    DefaultFullSharedAccessSignature
    DefaultListenSharedAccessSignature
  You can opt to use the DefaultListenSharedAccessSignature as a restricted listen-only connection string for your application
Notes: Talk about why you would not want to use the DefaultFullSharedAccessSignature. Remind students that the listen connection string can only listen to messages and cannot manage a notification hub.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 29: Registrations using the SDK
C#
await hub.RegisterNativeAsync(channelUri, tags);
Objective-C
[hub registerNativeWithDeviceToken:deviceTOken tags:nil completion:^(NSError* error) { if (error != nil) { NSLog(@”Error registering for notifications: %@”, error); } }];
Java
hub.register(regid, tags);
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 30: Registering from the Service Application
Registrations can occur from the application back-end instead of the client app
  Use NotificationHubClient.CreateClientFromConnectionString to get the hub client.
  Use the appropriate method on the hub client class
    CreateWindowsNativeRegistrationAsync
    CreateAppleNativeRegistrationAsync
  Use the channelUri, installationId and a unique user names
Notes: An example would be an application that uses a custom authentication scheme. You might want to build a Web API service for registration with Notification Hubs that authenticates the client application before you manually register them with the Notification Hub.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 31: Transient Registrations
Registrations have a time to live value that can be set to a maximum of 90 days
Registrations should be periodically refreshed.
  It’s typical to see a registration refreshed when an application is launched
Since registrations expire, it makes cleanup of registration on uninstall simple
Notes: Discussion Question: How would you design your application to handle registrations if the clients are expected to open your application multiple times within the same day?
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 32: Message Templates and Tags
Templates allow you to send a single message from a back-end and have it transformed into the correctly structured message for each platform
Templates use a binding format where you can specify where the message will appear in the XML or JSON content
  Custom properties can be used in the template
Clients can create multiple registrations to leverage different templates
Notes: Discussion Question: What are some reasons for using multiple templates for a single platform?
A good example would be an app that has one template for emergency alerts and another for typical app notifications.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 33: Message Templates and Tags (cont.)
Tags can be used to uniquely identify a client registration
When sending messages, tags can be leveraged to target the message to a specific set of devices:
  Broadcast – send message to all registrations
  Tag – send message to registrations that contain the specific tag
  Tag expression – send message to registrations whose set of tags match the specified expression
Notes: Discuss with the class some scenarios where they could use tags to filter the registrations that are targeted by a message.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 34: Lab: Using Queues and Service Bus to Manage Communication Between Web Applications in Azure
Estimated Time: 90 minutes
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 35: Lab Scenario
Now that you can generate sign-in sheets in worker roles, you need a scalable and consistent way to enqueue messages for the worker role. You have decided to use an Azure queue mechanism so that you can scale the worker roles in isolation to meet the demand of the queue size. In this lab, you will begin by implementing the communication between the Administration web application and the worker role by using Storage queues. Then you will replace that implementation with an implementation that uses Service Bus queues.
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 36: Lab Scenario
Currently, your on-premises Contoso Events application uses a WCF service to list the hotels that are near a location. You would like to continue to use the WCF service, but you cannot modify your company’s firewall. You also would not like to expose the true network location of the WCF service. You have decided to use Service Bus relays so that you have a common endpoint that you can provide to client applications. You will start by using that endpoint in your Contoso Events web application.
Notes: 20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 37: Lab Review
What are some of the ways that you can automate the change of your WCF bindings from their on-premises versions to a Service Bus Relay binding after the projects are published?
Notes: Question
What are some of the ways that you can automate the change of your WCF bindings from their on-premises versions to a Service Bus Relay binding after the projects are published?
Answer
With XML configuration, you can use transformations to change the binding to a relay equivalent when publishing. With C# configuration you can use dependency injection and an IoC container.
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus

## Slide 38: Module Review and Takeaways
Review Question(s) Reference Links
Notes: Review Question(s)
Question
Which queuing mechanism is better suited for storing large messages?
Answer
The Queue service in Azure Storage can store over 5 GB worth of messages in a queue.
Question
If you have an application that cannot afford to lose any messages, should you use the PeekLock or ReceiveAndDelete mode in your consuming client? How do you check to see if the message is a duplicate?
Answer
PeekLock allows you to retry messages that you might have failed to process. The MessageId of the message will be consistent across tries and allows you to determine if you are processing a duplicate message.
Question
You have a weather app and you are using Notification Hubs for messaging. You would like to let people within a specific area code receive an emergency alert about a hurricane. How should you architect your application to support this scenario?
Answer
First, you should start by designing the templates that specify how the notification should appear for the emergency alert message on each platform. Then the client applications can register by using that template and some location data (such as an area code) included in their tag(s). When an emergency alert needs to be sent out, you can use target-specific area codes in your tags and use the emergency message template to send a single message to notify all the targeted clients.
Reference Links: http://go.microsoft.com/fwlink/?LinkID=510217
20532C
8: Designing a Communication Strategy by Using Queues and Service Bus